## Slide 1: Fix Branch
CMPUT 229
University of Alberta

## Slide 2
Consider the original program below
1
2
3
4
5
foo:
beq t0 t1 target
addi t0 t0 1
target:
addi t1 t1 1
RISC-V Assembly
Address | Code | Basic
0x00400024 | 0x00628463 | beq x5, x6, 0x00000008
0x00400028 | 0x00128293 | addi x5, x5, 1
0x0040002c | 0x00130313 | addi x6, x6, 1
RARS
Address of branch target is 0x0040002c
Notes: Left side is the RISC-V assembly source code. Right side is what the code looks like after being assembled by RARS.

## Slide 3
After inserting three instructions, we obtain the modified program.
Address | Code | Basic
0x00400024 | 0x00628463 | beq x5, x6, 0x00000008
0x00400028 | 0x00128293 | addi x5, x5, 1
RARS
0x0040002c | 0x00128313 | addi x6, x5, 1
0x00400030 | 0x00130393 | addi x7, x6, 1
0x00400034 | 0x00138e13 | addi x28, x7, 1
0x0040002c | 0x00130313 | addi x6, x6, 1
0x00400038 | 0x00130313 | addi x6, x6, 1
Address of branch target is changed to 0x00400038
Branch offset did not change
Notes: Inserting instructions into the program changes the address of the branch target, but it did not change the branch offset.

## Slide 4: Task
RARS
Branch offset did not change
0x0040002c
0x00128293
addi x28, x7, 1
0x00400028
0x00400024
Address
0x00628463
Code
Basic
0x00400038
0x00400034
0x00400030
0x00138e13
0x00130393
addi x6, x6, 1
addi x6, x6, 1
addi x7, x6, 1
0x00130393
addi x6, x6, 1
beq x5, x6, 0x00000008
0x00130313
Adjust the offset such that the branch instruction branches to the same target label as it did in the original program
Notes: Need to adjust the branch offset so that the branch instruction branches to the same target label as it did in the original program.

## Slide 5: RISC-V Branch Instructions
beq | Branch EQual
bge | Branch Greater than or Equal
bgeu | Branch Greater than or Equal Unsigned
blt | Branch Less Than
bltu | Branch Less Than Unsigned
bne | Branch Not Equal
Notes: There are six types of branch instructions in RISC-V. These are also on the RISC-V reference data (‘green’) sheet.

## Slide 6: SB Type Format
All branch instructions are encoded in the SB Instruction Type Format
31 | 25 | 24 | 20 | 19 | 15 | 14 | 12 | 11 | 7 | 6 | 0
imm[12¦10:5] |  | rs2 |  | rs1 |  | funct3 |  | imm[4:1¦11] |  | opcode | 
The relative offset is encoded in bits 7-11 & 25-31 of the instruction

## Slide 7: SB Type Format - Limitations
Only 13 bits to to specify the offset (the lowest bit of the immediate is always zero)
  The distance between a branch instruction and its target is limited
Inserting instructions may push the target beyond the reach of the branch instruction
  Assume this will never the case in this lab
Notes: In this lab, the number of insertions to a program will never be enough to create a impossible branch.

## Slide 8: Jump Instructions
Inserting instruction can also affect jump instructions
You DO NOT need to adjust the immediate value of jump instructions in this lab
Notes: Jump instructions can also be affected by the insertion of instructions. Students do not need to adjust the immediate value of jump instructions in this lab. We will also never insert any branch or jump instructions to create the modified programs in this lab.

## Slide 9: Fixing Branch Instructions
A branch instruction only needs to be fixed if instructions are inserted between itself and the branch target
To calculate the address of the branch target, T, follow the algorithm below:
  L ← immediate of the branch instruction
  A ← L << 1
  S ← sign extend A to 32 bits
  T ← S + PC
Here, PC refers to the address that was used to load the instruction from memory
Notes: In the algorithm, PC refers to the address that was used to load the instruction from memory as opposed to the real value of PC when executing a program. This is because the common.s in this lab will load the programs from their files into the data segment.

## Slide 10: Insertion Points
Address of the instruction (in the original program) before a block of added instructions

## Slide 11: Insertion Points - Demonstration
Original Program
Modified Program
0x10010000
0x10010004
0x10010008
0x1001000c
0x10010010
foo: | addi t0 zero 1
 | addi t1 zero 2
 | bne t0 zero T1
 | add a7 t0 t1
T1: | jr ra
foo: | addi t0 zero 1
 | addi t1 zero 2
 | bne t0 zero T1
 | add a7 t0 t1
 | add t6 t3 t1
 | and t0 t3 t1
 | or t6 t3 t1
T1: | jr ra
Insertion point: [ ]
Number of instructions inserted: [ ]
0x1001000c
3

## Slide 12: Terminologies

## Slide 13: Different Types of Programs
The modified program is obtained by inserting instructions into the original program.
Branch instructions in the modified program must be fixed so that they jump to the same label as they did in the original program.
The fixed program refers to the modified program with fixed branch instructions.

## Slide 14: Instructions Array
The instructions array of a program is an array of RISC-V instructions in binary representation
The instructions in the array are the instructions in the program.

## Slide 15: Insertion Points Array
The insertion points array is an array of all the insertion points.
The array must be sorted in ascending order by the value of the insertion points.

## Slide 16: Insertions Array
The insertions array is an array of natural numbers
The i'th element in the array is the number of instructions inserted at the i'th insertion point in the insertion points array.

## Slide 17: Branches Array
The branches array contains the addresses of all the branch instructions in the original program.
Elements in the array must be sorted in ascending order by the addresses of the branch instructions.

## Slide 18: Targets Array
The targets array contains the addresses of the target instructions for all the branch instructions in the branches array.
The i'th element in the array is the address of the branch target for the i'th branch instruction in the branches array.

## Slide 19: An Important Note
All arrays are terminated by the sentinel value 0xFFFFFFFF

## Slide 20: Assignment
Students must implement all of the following functions

## Slide 21
fixBranch
  This function is the entry point of student's solution to this lab. It fixes branch instructions in the modified program such that they branch to the same target as they did in the original program. Writes the instructions of the fixed program program to a separate array.
  Arguments:
    a0: Pointer to the instructions array of the original program.
  a1: Pointer to the instructions array of the modified program.
  a2: Pointer to an empty array that is the same size as the instructions array
  of the modified program. This function must write the instructions of the
  fixed program to this array and terminate it with the sentinel value
  0xFFFFFFFF.
  Returns:
    None

## Slide 22
findInsertions
  Finds all the insertion points and how many instructions were inserted after each insertion point
  Arguments:
    a0: Pointer to the instructions array of the original program.
    a1: Pointer to the instructions array of the modified program.
  Returns:
    a0: Pointer to the insertion points array.
    a1: Pointer to the insertions array.

## Slide 23
findBranches
  Finds all the branches and their respective targets in the original program
  Arguments:
    a0: Pointer to the instructions array of the original program.
  Returns:
    a0: Pointer to the branches array
    a1: Pointer to the targets array

## Slide 24: Resources
We provide the two Python progams:
binDecompiler.py: a decompiler for RISC-V assembly.
hexToBin.py: converts hexadecimal numbers in textual format to binary format and writes the results to a file. Expects one hexadecimal number per line.

## Slide 25: Important Information
The webpage and README contains the specifications and example usages of the two Python programs in the previous slide.
The webpage also contains step-by-step instructions on how to create your own test cases and how to test you solution to the lab.

## Slide 26: Testing your Lab

## Slide 27: Input Guarantees
The binary representation of the RISC-V programs are terminated by the sentinel value 0xFFFFFFFF.
There will be a maximum of 50 instructions inserted to the modified program
There will be a maximum of 25 branches to fix.
All instructions are valid RISC-V instructions.
Neither branches nor jumps will ever be inserted to the original program to create the modified program.

## Slide 28
original.s
Start with a RISC-V .s file that satisfies the constraints outlined in the Input Guarantees slide

## Slide 29
original.s
1. Dump the source file into binary using RARS
rars a dump .text Binary original.bin original.s
original.bin
2. Decompile the binary file
original_decomp.tsv
original_decomp.txt
python3 binDecompiler.py b original.bin -o original_decomp
3. Create the modified program

## Slide 30: Creating the Modified Program
Option 1: Use a spreadsheet editor
  Google Spreadsheets
  Microsoft Excel
  Some IDE’s
Option 2: Use a plain text editor

## Slide 31: Option 1
Open original_decomp.tsv with a spreadsheet editor
Address | Code | Source
0x00400024 | 0x00628463 | beq x5, x6, 0x00000008
0x00400028 | 0x00128293 | addi x5, x5, 1
0x0040002c | 0x00130313 | addi x6, x6, 1
Address | Code | Source
0x00400024 | 0x00628463 | beq x5, x6, 0x00000008
0x00400028 | 0x00128293 | addi x5, x5, 1
 | 0x00128313 | 
 | 0x00130393 | 
 | 0x00138e13 | 
0x0040002c | 0x00130313 | addi x6, x6, 1
Insert hexadecimal representation of valid RISC-V instructions in the ‘Code’ column

## Slide 32: Option 2
Open original_decomp.txt with a plain text editor
0x00628463
0x00128293
0x00130313
Insert hexadecimal representation of valid RISC-V instructions
0x00628463
0x00128293
0x00128313
0x00130393
0x00138e13
0x00130313

## Slide 33
original.s
1. Dump the source file into binary using RARS
rars a dump .text Binary original.bin original.s
original.bin
2. Decompile the binary file
original_decomp.tsv
original_decomp.txt
python3 binDecompiler.py b original.bin -o original_decomp
3. Create the modified program
modified.txt
original_decomp.tsv
(modified)
Option 1
Option 2
Save as
4. Generate the binary file for the modified program
python3 hexToBin.py -i modified.txt -o modified.bin
Provide file name as command line argument
python3 hexToBin.py -o modified.bin
Provide instructions in the ‘Code’ column to standard input
modified.bin
5. Run fixBranch.s with the binary files of the orginal and the modified programs
lab.out
rars fixBranch.s pa original.bin modified.bin nc > lab.out
6. Check solution output
lab_out_decomp.tsv
lab_out_decomp.txt
python3 binDecompiler.py h lab.out -o lab_out_decomp