## Slide 1: Branch Counting
CMPUT 229
University of Alberta

## Slide 2
1
2
3
4
5
6
7
8
9
foo:
bge t0 t1 target
addi t0 t0 1
j foo
target:
addi t1 t1 1
li t0 0
li t2 10
blt t1 t2 foo
RISC-V Assembly
Consider the program below
Forward Branch
Backward Branch

## Slide 3
RARS
Now consider how branch targets are stored in assembly
Positive Offset
0x00400000+0x0000000c
=0x0040000c
Negative Offset
0x00400018+0xffffffe8
=0x00400000
Address | Code | Basic
0x00400000 | 0x0062d663 | bge x5 x6 0x0000000c
0x00400004 | 0x00128293 | addi x5 x5 1
0x00400008 | 0xff9ff06f | jal x0 0xfffffff8
0x0040000c | 0x00130313 | addi x6 x6 1
0x00400010 | 0x00000293 | addi x5 x0 0
0x00400014 | 0x00a00393 | addi x7 x0 10
0x00400018 | 0xfe7344e3 | blt x6 x7 0xffffffe8

## Slide 4: Task
Identify branches by their opcode, and use the offset to determine if the branch goes forwards or backwards.

## Slide 5: RISC-V Branch Instructions
beq | Branch EQual
bge | Branch Greater than or Equal
bgeu | Branch Greater than or Equal Unsigned
blt | Branch Less Than
bltu | Branch Less Than Unsigned
bne | Branch Not Equal

## Slide 6: SB Type Format
All branch instructions are encoded in the SB Instruction Type Format
31 | 25 | 24 | 20 | 19 | 15 | 14 | 12 | 11 | 7 | 6 | 0
imm[12¦10:5] | rs2 | rs1 | funct3 | imm[4:1¦11] | opcode
The relative offset is encoded in bits 7-11 & 25-31 of the instruction

## Slide 7: Assignment
Students must implement the branchCounting function

## Slide 8: Instructions Array
The instructions array of a program is an array of RISC-V instructions in binary representation
The instructions in the array are the instructions in the input program
The array is terminated by the sentinel value 0xFFFFFFFF

## Slide 9
branchCounting
  This function is the entry point of student's solution to this lab. It counts forward and backward branches in the program pointed to by a0. Returns the number of forward branches in a0 and the number of backward branches in a1.
  Arguments:
    a0: Pointer to the instructions array of the input program.
  Returns:
    a0: Integer number of forward branches in input.
    a1: Integer number of backward branches in input.

## Slide 10: Input Guarantees
The instructions array is terminated by the sentinel value 0xFFFFFFFF.
All instructions in the input file are valid RISC-V instructions.
No branches will have an offset of zero.
There are at most 100 instructions in the input file.

## Slide 11: Testing Workflow
You can generate input files from any RISCV .s file satisfying input guarantees. To generate the binary file, test.bin, for the test program, test.s, you can run the following command:
rars a dump .text Binary test.bin test.s
Run your solution on the input file with
rars branchCounting.s pa test.bin nc > lab.out