## Slide 1: Lab #5: Control Flow Graph
CMPUT 229

## Slide 2
What is a Control Flow Graph?
A Control Flow Graph (CFG) shows all the possible execution paths of a program.

## Slide 3
Basic Blocks
A basic block is a segment of code where instructions execute in order from start to finish.
Once execution enters a block, all instructions in the block must be executed.
Only the first instruction of a basic block can be the target for a branch or jump instruction.
The nodes of a CFG are basic blocks.

## Slide 4
Edges
Edges denote directed control flow between basic blocks.
There are two types of edges:
- forward edge
- back edge.
Branches and jumps redirect control flow, creating multiple execution paths within a program.

## Slide 5
Successors & Predecessors
A successor of a block Bi is any block that can be reached from Bi.
The concepts of predecessor and immediate predecessor are analogous.
An immediate successor of a block Bi directly follows Bi.
Successors of B0
Immediate successors of B0
addi t0, zero, 10
addi t1, zero, 0
blt t0, zero, loop

## Slide 6
Successors & Predecessors
A successor of a block Bi is any block that can be reached from Bi.
The concepts of predecessor and immediate predecessor are analogous.
An immediate successor of a block Bi directly follows Bi.
Successors of B0
Immediate successors of B0
addi t0, zero, 10
addi t1, zero, 0
blt t0, zero, loop
B1
addi t1, zero, -1
J exit
B0

## Slide 7: Assignment
Lab #5: Control Flow Graph

## Slide 8
Overview
Goal: to generate control flow information for a single function.
Each function’s implementation should accurately populate these custom data structures.
These functions will populate data structures that represent control flow constructs:
            - basic blocks, edges, successors, and predecessors.
The common.s file initializes the data structures and runs tests on your implementation. It also helps to parse the populated data structures.

## Slide 9: Overview
Goal: generate control flow information for a single function.
Task: write functions that populate data structures that represent control flow constructs:
  Basic blocks
  Edges
  Successors
  Predecessors
Resources: the common.s file:
  initializes the data structures
  runs tests on your implementation
  helps to parse the populated data structures.

## Slide 10
A Sample Input Function
The _basicblocks function below serves as an example of an intended input for the lab. It will be used as a reference to explain the custom data structures.

## Slide 11
Basic Block Leaders
The first statement in a function
Any statement that is the target of a branch/jump
Any statement that immediately follows a branch or jump
Basic-block leaders:

## Slide 12
Forming Basic Blocks
A basic-block is a leader and all instructions after the leader up to, but not including the next leader.
B0
B1

## Slide 13
Building the Control Flow Graph
A basic-block is a leader and all instructions after the leader up to, but not including the next leader.
B0
B1

## Slide 14
Basic Block Identifiers
To uniquely identify blocks, we use the offsets (in words) of their leaders from the function’s base address in memory.
E.g., The second block starts 3 words away from the function’s base address so its ID is 3.

## Slide 15
Pseudo-instructions in RISC-V simplify assembly code by representing higher-level operations.
Labels are symbolic pointers to specific instructions used for branch or jump offsets and do not appear in the executable code. They are also used to simplify assembly.
For example, 'mv t0, zero' translates to 'add t0, zero, zero' during assembly, which copies the value 0 into the register t0 as well.
Pseudo Instructions and Labels
Notes: Note on beqz a0, End instruction translation.
The offset for the instruction seems confusing for branches. The beqz a0, End instruction should move the program counter two instructions ahead to mv a0, s0. However, the offset for this instruction is only 4. This seems to suggest that the beqz a0, End instruction moves the PC to the j loop instruction.
This is a confusing situation because by default, branch instructions increment the PC by 4. Thus, the offset of 4 will actually point 2 instructions ahead as we intended.

## Slide 16: Decoding Instructions
RISC-V instruction formats are differentiated by their opcode, while funct3 distinguishes instructions within each format.
Decoding the fourth instruction (0x0012f393) of the _basicblocks function as an example:
funct3 = 111 (andi instruction)
opcode = 001 0011 (I-type instruction)
0x0012f393 = 0000 0000 0001 0010 1111 0011 1001 0011

## Slide 17: Data Structures
Lab #5: Control Flow Graph

## Slide 18
instructionsArray
An array of words that contains the instructions of the input function.
Ends with a sentinel value of -1.

## Slide 19: leadersArray
An array of bytes representing the leadership status of each instruction.
Each byte corresponds directly to an instruction in the instructionsArray.
If an instruction is a leader, its corresponding byte will be 1; otherwise, it will be 0.
Ends with a sentinel value of -1.

## Slide 20
edgesList
A 2D byte array which stores all the edges within a function’s CFG.
Ends with a sentinel value of -1 in both bytes.
In an entry: the first byte indicates the source, and the second byte indicates the target.

## Slide 21
successorsTable
In an entry: the first byte indicates the block, followed by 2 bytes for its successorsList.
A 2D byte array storing immediate successors for each basic block in a function's CFG.
Each successorsList ends with -1, while the basic blocks column ends with -2 (indicating the table’s end).
Notes: A 2D array of bytes initialized to -1 (0XFF).
Each entry in the table corresponds to a basic block, where the first byte indicates the block, and the following 2 bytes store its successorsList (a list of its immediate successor blocks).
Every basic block within the CFG is represented, regardless of whether it has successors.
Every basic block's successorsList ends with -1.
The table ends with a sentinel value of -2 (0xFE) in column reserved for basic blocks.

## Slide 22
predecessorsTable
Each predecessorsList ends with -1, while the basic blocks column ends with -2 (indicating the table’s end).
A 2D byte array storing immediate predecessors for each basic block in a function's CFG.
In an entry: the first byte indicates the block, followed by 4 bytes for its predecessorsList.
Notes: A 2D array of bytes initialized to -1 (0XFF).
Each entry in the table corresponds to a basic block, where the first byte indicates the block, and the following 4 bytes store its predecessorsList (a list of its immediate predecessor blocks).
Every basic block within the CFG is represented, regardless of whether it has predecessors.
Every basic block's predecessorsList ends with -1 (0xFF).
The table ends with a sentinel value of -2 (0xFE) in the basic blocks column.

## Slide 23: Function Signatures
Lab #5: Control Flow Graph

## Slide 24
getControlFlowGraph
a0: a pointer to the instructionsArray
Arguments:
Returns:
The main function called from common.s to retrieve information about a function's control flow graph.
Description:
a1: a pointer to the leadersArray
a2: a pointer to the edgesList
a3: a pointer to the successorsTable
a4: a pointer to the predecessorsTable
None

## Slide 25
getLeaders
a0: a pointer to the instructionsArray
Arguments:
Returns:
Identifies the basic block leaders within a function's instructions.
Description:
a1: a pointer to the leadersArray
None

## Slide 26
getEdges
a0: a pointer to the instructionsArray
Arguments:
Returns:
Creates a list of edges between basic blocks within a function's control flow graph.
Description:
a1: a pointer to the leadersArray
None
a2: a pointer to the edgesList

## Slide 27
getSuccessors
a0: a pointer to the instructionsArray
Arguments:
Returns:
Creates a list of immediate successors for each basic block within a function’s control flow graph.
Description:
a1: a pointer to the leadersArray
None
a2: a pointer to the successorsTable

## Slide 28
getPredecessors
a0: a pointer to the instructionsArray
Arguments:
Returns:
Creates a list of immediate predecessors for each basic block within a function’s control flow graph.
Description:
a1: a pointer to the leadersArray
None
a2: a pointer to the predecessorsTable

## Slide 29
getBranchImm (helper)
a0: a branch instruction word
a0: a sign extended immediate
Arguments:
Returns:
Takes a branch instruction (SB-type) and extracts the sign-extended immediate
Description:

## Slide 30
getJalImm (optional helper)
a0: a jal instruction word
a0: a sign extended immediate
Arguments:
Returns:
Takes a jump instruction (UJ-type) and extracts the sign-extended immediate
Description:

## Slide 31: Testing
Lab #5: Control Flow Graph

## Slide 32: Program Arguments
We have provided some test inputs and expected outputs in the Tests folder.
One argument required for controlFlowGraph.s: the full path to the binary file of an assembled RISC-V function.
Ensure there are no quotation marks or spaces in the path.

## Slide 33: Unit Tests
The common.s file will run unit tests on the functions in controlFlowGraph.s.
You can view the results in the “Run I/O” panel of RARS.
Check out the .data section in the common.s file to see how they are set up.
Tests are hardcoded and do not use the file set as the program argument.

## Slide 34: Parsed Control Flow Graph
The common.s file also parses the data structures populated by controlFlowGraph.s.
You can view the results in the “Run I/O” panel of RARS following the unit tests.
All structures must end with a sentinel value to be parsed properly.

## Slide 35: Tests Folder
There are three tests: basicblocks, nestedloop, singleinstruction.
A .out file containing the correct output for the test.
A .bin (binary) file containing the assembled function (program argument).
- A .s file containing the assembly code of the input function.
Each test has the following:

## Slide 36: Creating Tests
Unit tests and provided tests are not extensive.
You can now execute controlFlowGraph.s with the program argument set to the full path of test.bin.
Write the test function in assembly file (e.g., test.s).
To create a test, do the following:
Create the binary file for your function i.e., execute the command “rars a dump .text Binary test.bin test.s”.
Create your own tests to ensure your lab handles corner cases as well.

## Slide 37: Disassembler
Lab #5: Control Flow Graph

## Slide 38: What is a Disassembler?
RARS is a RISC-V Assembler that translates RISC-V instructions to executable binary.
For this lab, we will use an Open-Source RISC-V Disassembler (https://github.com/michaeljclark/riscv-disassembler)
A Disassembler does the opposite.

## Slide 39: How to Use the Disassembler
There is a Disassembly folder in the Code folder.
There is a file called “print-instructions.c” in this folder that prints the equivalent instructions for hexadecimal words.
First, compile “print-instructions.c” i.e., execute the command “gcc print-instructions.c”
Next, create a text file containing hexadecimal instructions. The file should look like this:

## Slide 40: How to Use the Disassembler (cont.)
Once you have an executable for print-instructions.c (a.out) and a text file with hexadecimal instructions (example.txt), execute “./a.out example.txt”
Here is the disassembled instructions from example.txt:

## Slide 41: Notes on the Disassembler
The disassembler translates addi t0, t0, 0 to mv t0, zero. Keep this in mind to avoid confusion with addi instructions.
The disassembler will not translate a sentinel value (0xFFFFFFFF) as expected.

## Slide 42: What to Submit?
A single file, called controlFlowGraph.s.
Do not modify the line .include "common.s".
Do not modify the common.s file.
Do not modify the name of any function.
Push your repository to GitHub before the deadline.
Do not remove the CMPUT 229 Student Submission License.
Keep the file in the Code folder of the git repository.

## Slide 43: Good Luck!
Lab #5: Control Flow Graph